## Slide 1
HOW TO READ THE REPORT
The reported clock starts after VAD
VAD endpointing is excluded because the test used synthetic clean trailing silence.
Post-VAD time to first audio = SLM TTFT + SLM generation + [cloud LLM] + response preparation
Stage duration | What it measures
Reported statistics | Each result cell shows P50 / P90 / Max from left to right
SLM TTFT | Finalized audio → first meaningful SLM token
SLM generation | First → last SLM token; TPS = (output tokens − 1) / this duration
Cloud LLM | Only for non_tool; SLM completion → complete Gemini response
Response preparation | Cloud TTS or cached reply → first response-audio byte
“Audio → …” means VAD-ready audio → milestone. It does not include speaking time or VAD endpointing.
Measured on Jetson AGX Orin · 14 Aug 2026 · VAD endpoint latency excluded
01
Notes: All displayed latency begins when VAD has finalized the waveform. The previous endpoint-delay result was removed because the runner appended synthetic zero-valued silence, which does not represent a naturally noisy robot environment. The equation uses non-overlapping post-VAD stage durations; cumulative milestone columns should not be summed. Audio-to-last-audio is intentionally omitted.

## Slide 2
TOOL-CALL SUMMARY · ALL AUDIO LENGTHS
50% MPS keeps tool calls interactive
64 measured turns per scheduling condition · every result cell is P50 / P90 / Max
GPU scheduling condition | Audio → 1st SLM P50 / P90 / Max | 1st → last SLM P50 / P90 / Max | SLM TPS P50 / P90 / Max | Audio → last SLM P50 / P90 / Max | Audio → 1st audio P50 / P90 / Max
Full GPU MPS off | 202 / 211 / 236 | 332 / 563 / 564 | 114.9 / 146.5 / 146.7 | 534 / 748 / 750 | 568 / 782 / 784
MPS 70% | 209 / 224 / 243 | 351 / 596 / 596 | 108.6 / 138.2 / 138.5 | 561 / 792 / 794 | 596 / 827 / 828
MPS 50% | 219 / 234 / 254 | 376 / 638 / 639 | 101.5 / 129.3 / 129.4 | 595 / 841 / 843 | 632 / 879 / 880
MPS 30% | 358 / 381 / 409 | 696 / 1,178 / 1,179 | 54.8 / 69.8 / 69.9 | 1,054 / 1,489 / 1,491 | 1,116 / 1,551 / 1,553
At the 50% MPS cap, P50 is 219 ms to first SLM token, 595 ms to the completed tool call, and 632 ms to first cached audio.
All 8 audio lengths pooled · 64 warm measured turns per condition · VAD and last audio excluded
02
Notes: This is the aggregate tool-call view requested for a single overall distribution across every tested audio length. Each cell reads P50, P90, and maximum from left to right. The 50% MPS active-thread cap remains close to full-thread execution, while 30% materially increases generation and completion latency. These are project measurements from the controlled tool-call corpus; the detailed per-length slides follow.

## Slide 3
TOOL-CALL RESULTS · FULL GPU · MPS OFF
Full-GPU baseline keeps TTFT near 0.2 seconds
MPS disabled · 114.9 tok/s aggregate decode · 568 ms to first cached audio · each cell shows P50 / P90 / Max
Audio length | Audio → 1st SLM P50 / P90 / Max | 1st → last SLM P50 / P90 / Max | SLM TPS P50 / P90 / Max | Audio → last SLM P50 / P90 / Max | Audio → 1st audio P50 / P90 / Max
1.39 s | 193 / 194 / 194 | 217 / 217 / 217 | 124.7 / 124.7 / 124.8 | 410 / 410 / 410 | 443 / 443 / 444
2.00 s | 235 / 235 / 236 | 191 / 191 / 191 | 146.6 / 146.6 / 146.7 | 426 / 426 / 427 | 460 / 460 / 460
3.00 s | 193 / 194 / 194 | 204 / 204 / 205 | 137.3 / 137.4 / 137.4 | 397 / 398 / 398 | 431 / 431 / 431
4.00 s | 201 / 202 / 202 | 294 / 294 / 294 | 119.2 / 119.3 / 119.3 | 495 / 495 / 495 | 528 / 529 / 529
5.00 s | 204 / 204 / 204 | 371 / 371 / 371 | 110.6 / 110.6 / 110.7 | 574 / 575 / 575 | 608 / 609 / 610
6.00 s | 206 / 207 / 208 | 371 / 371 / 372 | 110.5 / 110.5 / 110.5 | 578 / 578 / 579 | 612 / 613 / 613
6.75 s | 211 / 212 / 212 | 537 / 538 / 538 | 96.8 / 96.8 / 96.8 | 748 / 749 / 750 | 782 / 783 / 784
7.44 s | 183 / 184 / 184 | 564 / 564 / 564 | 95.8 / 95.9 / 95.9 | 747 / 748 / 748 | 781 / 782 / 782
Statistics: P50 / P90 / Max · 8 runs per audio · TPS excludes TTFT · VAD and last audio excluded
03
Notes: This slide shows the controlled tool-call path on the direct full-GPU baseline with MPS disabled. Audio length remains visible rather than being aggregated away. The aggregate decode rate is MPS disabled · 114.9 tokens per second. Longer input audio does not automatically increase TTFT; the structured output length controls most of the first-to-last-token gap. Audio-to-last-audio is omitted because it is derived from response WAV duration rather than acoustic loopback.

## Slide 4
TOOL-CALL RESULTS · 70% MPS CAP
70% MPS closely tracks full-thread latency
108.6 tok/s aggregate decode · only +28 ms to first audio vs 100% · each cell shows P50 / P90 / Max
Audio length | Audio → 1st SLM P50 / P90 / Max | 1st → last SLM P50 / P90 / Max | SLM TPS P50 / P90 / Max | Audio → last SLM P50 / P90 / Max | Audio → 1st audio P50 / P90 / Max
1.39 s | 198 / 199 / 199 | 229 / 229 / 229 | 117.9 / 118.0 / 118.0 | 427 / 428 / 428 | 462 / 463 / 463
2.00 s | 242 / 243 / 243 | 202 / 203 / 203 | 138.5 / 138.5 / 138.5 | 444 / 445 / 445 | 480 / 480 / 480
3.00 s | 202 / 202 / 203 | 216 / 216 / 216 | 129.7 / 129.8 / 129.8 | 418 / 418 / 419 | 452 / 453 / 453
4.00 s | 208 / 209 / 210 | 310 / 311 / 311 | 112.7 / 112.8 / 113.0 | 519 / 519 / 520 | 553 / 554 / 555
5.00 s | 210 / 211 / 211 | 392 / 393 / 393 | 104.6 / 104.6 / 104.6 | 602 / 603 / 603 | 637 / 638 / 638
6.00 s | 214 / 214 / 214 | 392 / 392 / 393 | 104.5 / 104.5 / 104.6 | 606 / 607 / 607 | 641 / 642 / 642
6.75 s | 224 / 224 / 225 | 569 / 569 / 569 | 91.4 / 91.5 / 91.5 | 793 / 793 / 794 | 828 / 828 / 828
7.44 s | 189 / 189 / 189 | 596 / 596 / 596 | 90.6 / 90.6 / 90.6 | 785 / 785 / 786 | 820 / 820 / 821
Statistics: P50 / P90 / Max · 8 runs per audio · TPS excludes TTFT · VAD and last audio excluded
04
Notes: This slide shows the controlled tool-call path at a 70% CUDA MPS active-thread cap. Audio length remains visible rather than being aggregated away. The aggregate decode rate is 108.6 tokens per second. Longer input audio does not automatically increase TTFT; the structured output length controls most of the first-to-last-token gap. Audio-to-last-audio is omitted because it is derived from response WAV duration rather than acoustic loopback.

## Slide 5
TOOL-CALL RESULTS · 50% MPS CAP
50% MPS remains interactive at 101.5 tok/s
632 ms from VAD-ready audio to first cached audio · +64 ms vs 100% · each cell shows P50 / P90 / Max
Audio length | Audio → 1st SLM P50 / P90 / Max | 1st → last SLM P50 / P90 / Max | SLM TPS P50 / P90 / Max | Audio → last SLM P50 / P90 / Max | Audio → 1st audio P50 / P90 / Max
1.39 s | 206 / 207 / 207 | 245 / 245 / 245 | 110.1 / 110.2 / 110.2 | 451 / 452 / 452 | 487 / 488 / 488
2.00 s | 254 / 254 / 254 | 217 / 217 / 217 | 129.3 / 129.4 / 129.4 | 470 / 471 / 471 | 507 / 508 / 508
3.00 s | 211 / 212 / 213 | 231 / 231 / 232 | 121.2 / 121.4 / 121.5 | 443 / 443 / 443 | 479 / 480 / 480
4.00 s | 218 / 219 / 219 | 332 / 332 / 332 | 105.4 / 105.4 / 105.5 | 550 / 551 / 551 | 587 / 587 / 587
5.00 s | 220 / 221 / 221 | 420 / 420 / 420 | 97.7 / 97.7 / 97.7 | 640 / 640 / 640 | 677 / 678 / 678
6.00 s | 224 / 224 / 224 | 421 / 421 / 421 | 97.5 / 97.5 / 97.5 | 644 / 645 / 645 | 682 / 682 / 683
6.75 s | 234 / 234 / 234 | 608 / 608 / 608 | 85.5 / 85.5 / 85.5 | 842 / 842 / 843 | 879 / 879 / 880
7.44 s | 197 / 199 / 200 | 639 / 639 / 639 | 84.5 / 84.6 / 84.7 | 836 / 837 / 837 | 873 / 874 / 875
Statistics: P50 / P90 / Max · 8 runs per audio · TPS excludes TTFT · VAD and last audio excluded
05
Notes: This slide shows the controlled tool-call path at a 50% CUDA MPS active-thread cap. Audio length remains visible rather than being aggregated away. The aggregate decode rate is 632 ms from VAD-ready audio to first cached audio · +64 ms vs 100% tokens per second. Longer input audio does not automatically increase TTFT; the structured output length controls most of the first-to-last-token gap. Audio-to-last-audio is omitted because it is derived from response WAV duration rather than acoustic loopback.

## Slide 6
TOOL-CALL RESULTS · 30% MPS CAP
30% MPS slows long structured calls
54.8 tok/s aggregate decode · longest calls need about 1.49 s to finish · each cell shows P50 / P90 / Max
Audio length | Audio → 1st SLM P50 / P90 / Max | 1st → last SLM P50 / P90 / Max | SLM TPS P50 / P90 / Max | Audio → last SLM P50 / P90 / Max | Audio → 1st audio P50 / P90 / Max
1.39 s | 322 / 323 / 323 | 454 / 455 / 455 | 59.4 / 59.5 / 59.5 | 777 / 778 / 778 | 838 / 838 / 839
2.00 s | 408 / 409 / 409 | 401 / 401 / 401 | 69.9 / 69.9 / 69.9 | 809 / 809 / 809 | 870 / 871 / 871
3.00 s | 348 / 348 / 349 | 428 / 429 / 429 | 65.4 / 65.4 / 65.4 | 776 / 777 / 777 | 837 / 838 / 838
4.00 s | 357 / 358 / 358 | 615 / 616 / 616 | 56.9 / 56.9 / 56.9 | 973 / 973 / 974 | 1,034 / 1,035 / 1,035
5.00 s | 359 / 360 / 360 | 777 / 777 / 777 | 52.8 / 52.8 / 52.8 | 1,136 / 1,137 / 1,138 | 1,198 / 1,198 / 1,198
6.00 s | 363 / 364 / 364 | 777 / 777 / 778 | 52.8 / 52.8 / 52.8 | 1,140 / 1,141 / 1,141 | 1,202 / 1,203 / 1,203
6.75 s | 364 / 365 / 365 | 1,124 / 1,124 / 1,124 | 46.3 / 46.3 / 46.3 | 1,487 / 1,488 / 1,489 | 1,549 / 1,549 / 1,550
7.44 s | 311 / 312 / 313 | 1,179 / 1,179 / 1,179 | 45.8 / 45.8 / 45.8 | 1,490 / 1,491 / 1,491 | 1,551 / 1,552 / 1,553
Statistics: P50 / P90 / Max · 8 runs per audio · TPS excludes TTFT · VAD and last audio excluded
06
Notes: This slide shows the controlled tool-call path at a 30% CUDA MPS active-thread cap. Audio length remains visible rather than being aggregated away. The aggregate decode rate is 54.8 tokens per second. Longer input audio does not automatically increase TTFT; the structured output length controls most of the first-to-last-token gap. Audio-to-last-audio is omitted because it is derived from response WAV duration rather than acoustic loopback.

## Slide 7
NON-TOOL SUMMARY · ALL AVAILABLE RUNS
Cloud and TTS dominate the non-tool path
Runs: full GPU=30 · MPS70=30 · MPS50=18 · MPS30=10 · every cell is P50 / P90 / Max
GPU scheduling condition | Audio → 1st SLM P50 / P90 / Max | 1st → last SLM P50 / P90 / Max | SLM TPS P50 / P90 / Max | Audio → last SLM P50 / P90 / Max | Audio → cloud* P50 / P90 / Max | Audio → 1st audio P50 / P90 / Max
Full GPU MPS off | 200 / 212 / 215 | 462 / 615 / 617 | 99.5 / 134.9 / 135.2 | 667 / 827 / 830 | 2,941 / 3,601 / 4,733 | 5,242 / 5,975 / 7,096
MPS 70% | 219 / 227 / 228 | 487 / 651 / 651 | 94.4 / 127.2 / 127.4 | 707 / 878 / 880 | 3,392 / 3,963 / 4,059 | 5,724 / 6,263 / 6,545
MPS 50% | 202 / 235 / 237 | 518 / 692 / 692 | 88.8 / 119.6 / 119.6 | 711 / 898 / 928 | 2,998 / 3,711 / 3,963 | 5,278 / 6,066 / 6,390
MPS 30% | 360 / 370 / 370 | 966 / 1,288 / 1,288 | 47.6 / 64.1 / 64.1 | 1,326 / 1,659 / 1,659 | 3,637 / 4,066 / 4,368 | 6,019 / 6,413 / 6,616
On the full-GPU baseline (MPS off), SLM routing completes at 667 ms P50; dynamic cloud speech starts at 5.24 s P50.
*Gemini response completion · unequal repetitions by condition · external cloud/network/TTS latency · VAD/last audio excluded
07
Notes: This is the aggregate non-tool view across every available valid cloud-path run. Each cell reads P50, P90, and maximum from left to right. The local SLM decision remains much faster than the complete dynamic response path; Gemini, Wi-Fi, and laptop OmniVoice dominate the time to first audio. Do not rank MPS caps using the cloud columns: p50 has fewer repetitions, and external latency is uncontrolled. The 30% condition now covers all five audio lengths but still has only two repetitions per length.

## Slide 8
NON-TOOL RESULTS · FULL GPU · MPS OFF
Cloud + TTS dominate the full-GPU baseline
MPS disabled · 99.5 tok/s SLM decode · Gemini 2.13 s median · 6 uncached runs per audio length
Audio length | Audio → 1st SLM P50 / P90 / Max | 1st → last SLM P50 / P90 / Max | SLM TPS P50 / P90 / Max | Audio → last SLM P50 / P90 / Max | Audio → cloud* P50 / P90 / Max | Audio → 1st audio P50 / P90 / Max
1.0 s | 192 / 197 / 200 | 178 / 180 / 181 | 134.9 / 135.2 / 135.2 | 371 / 376 / 381 | 2,123 / 2,174 / 2,191 | 4,151 / 4,422 / 4,534
3.0 s | 198 / 200 / 200 | 319 / 321 / 321 | 109.9 / 109.9 / 110.0 | 518 / 518 / 518 | 2,942 / 3,326 / 3,464 | 5,035 / 5,479 / 5,663
5.0 s | 205 / 209 / 209 | 462 / 467 / 473 | 99.5 / 99.9 / 100.1 | 667 / 670 / 671 | 3,285 / 3,615 / 3,752 | 5,473 / 5,978 / 6,219
7.0 s | 210 / 210 / 210 | 577 / 579 / 579 | 95.2 / 95.5 / 95.5 | 787 / 789 / 789 | 3,197 / 4,401 / 4,733 | 5,631 / 6,782 / 7,096
7.5 s | 212 / 214 / 215 | 615 / 617 / 617 | 94.2 / 94.4 / 94.4 | 827 / 829 / 830 | 2,973 / 3,538 / 3,584 | 5,260 / 5,932 / 5,948
Cloud / network / laptop TTS are external; compare SLM TTFT, generation, and TPS across local scheduling conditions—not cloud totals.
Statistics: P50 / P90 / Max · *Gemini cloud completion, not observed last-token time · VAD/last audio excluded
08
Notes: This slide shows the non-tool path on the direct full-GPU baseline with MPS disabled. The local SLM timings can be compared across local scheduling conditions, but Gemini, Wi-Fi, and laptop OmniVoice timings cannot be controlled by them. Gemini returned a complete non-streamed response, so the cloud milestone is response completion rather than a separately observed last token. P90 is linearly interpolated; the 30% non-tool P90 has only two runs and is descriptive, not a stable tail estimate.

## Slide 9
NON-TOOL RESULTS · 70% MPS CAP
70% MPS keeps local routing fast
94.4 tok/s SLM decode · external Gemini, Wi-Fi, and TTS remain variable · 6 uncached runs per audio length
Audio length | Audio → 1st SLM P50 / P90 / Max | 1st → last SLM P50 / P90 / Max | SLM TPS P50 / P90 / Max | Audio → last SLM P50 / P90 / Max | Audio → cloud* P50 / P90 / Max | Audio → 1st audio P50 / P90 / Max
1.0 s | 199 / 200 / 200 | 189 / 189 / 189 | 127.2 / 127.3 / 127.4 | 388 / 388 / 389 | 2,255 / 2,751 / 3,102 | 4,453 / 4,890 / 5,025
3.0 s | 205 / 205 / 206 | 338 / 338 / 338 | 103.6 / 103.7 / 103.7 | 543 / 543 / 543 | 3,426 / 3,834 / 3,874 | 5,724 / 5,941 / 6,074
5.0 s | 220 / 220 / 220 | 487 / 487 / 488 | 94.4 / 94.4 / 94.4 | 707 / 707 / 708 | 3,733 / 3,973 / 3,976 | 6,055 / 6,289 / 6,320
7.0 s | 226 / 226 / 227 | 610 / 610 / 610 | 90.1 / 90.1 / 90.1 | 836 / 836 / 837 | 3,639 / 4,010 / 4,059 | 6,019 / 6,513 / 6,545
7.5 s | 227 / 228 / 228 | 651 / 651 / 651 | 89.1 / 89.1 / 89.1 | 878 / 879 / 880 | 3,264 / 3,565 / 3,654 | 5,725 / 6,014 / 6,078
Cloud / network / laptop TTS are external; compare SLM TTFT, generation, and TPS across local scheduling conditions—not cloud totals.
Statistics: P50 / P90 / Max · *Gemini cloud completion, not observed last-token time · VAD/last audio excluded
09
Notes: This slide shows the non-tool path at a 70% CUDA MPS active-thread cap. The local SLM timings can be compared across local scheduling conditions, but Gemini, Wi-Fi, and laptop OmniVoice timings cannot be controlled by them. Gemini returned a complete non-streamed response, so the cloud milestone is response completion rather than a separately observed last token. P90 is linearly interpolated; the 30% non-tool P90 has only two runs and is descriptive, not a stable tail estimate.

## Slide 10
NON-TOOL RESULTS · 50% MPS CAP
50% MPS preserves local routing
88.8 tok/s SLM decode · post-VAD TTFT remains about 0.19–0.21 s · runs by length: 4 / 4 / 3 / 3 / 4
Audio length | Audio → 1st SLM P50 / P90 / Max | 1st → last SLM P50 / P90 / Max | SLM TPS P50 / P90 / Max | Audio → last SLM P50 / P90 / Max | Audio → cloud* P50 / P90 / Max | Audio → 1st audio P50 / P90 / Max
1.0 s | 196 / 207 / 208 | 201 / 201 / 201 | 119.6 / 119.6 / 119.6 | 396 / 408 / 408 | 2,220 / 2,285 / 2,303 | 4,194 / 4,431 / 4,503
3.0 s | 214 / 214 / 214 | 359 / 359 / 359 | 97.5 / 97.5 / 97.5 | 573 / 573 / 574 | 3,128 / 3,528 / 3,678 | 5,257 / 5,732 / 5,889
5.0 s | 194 / 223 / 230 | 518 / 518 / 518 | 88.8 / 88.8 / 88.8 | 711 / 741 / 748 | 3,560 / 3,882 / 3,963 | 5,960 / 6,304 / 6,390
7.0 s | 197 / 228 / 235 | 649 / 649 / 649 | 84.8 / 84.8 / 84.8 | 846 / 876 / 884 | 3,292 / 3,688 / 3,787 | 6,014 / 6,154 / 6,189
7.5 s | 215 / 236 / 237 | 692 / 692 / 692 | 83.8 / 83.9 / 83.9 | 906 / 928 / 928 | 3,009 / 3,148 / 3,163 | 5,412 / 5,585 / 5,615
Cloud / network / laptop TTS are external; compare SLM TTFT, generation, and TPS across local scheduling conditions—not cloud totals.
Statistics: P50 / P90 / Max · *Gemini cloud completion, not observed last-token time · VAD/last audio excluded
10
Notes: This slide shows the non-tool path at a 50% CUDA MPS active-thread cap. The local SLM timings can be compared across local scheduling conditions, but Gemini, Wi-Fi, and laptop OmniVoice timings cannot be controlled by them. Gemini returned a complete non-streamed response, so the cloud milestone is response completion rather than a separately observed last token. P90 is linearly interpolated; the 30% non-tool P90 has only two runs and is descriptive, not a stable tail estimate.

## Slide 11
NON-TOOL RESULTS · 30% MPS CAP
30% MPS slows SLM routing
local SLM decode falls to 45–64 tok/s by audio length · 2 uncached runs per audio length
Audio length | Audio → 1st SLM P50 / P90 / Max | 1st → last SLM P50 / P90 / Max | SLM TPS P50 / P90 / Max | Audio → last SLM P50 / P90 / Max | Audio → cloud* P50 / P90 / Max | Audio → 1st audio P50 / P90 / Max
1.0 s | 324 / 325 / 325 | 374 / 374 / 375 | 64.1 / 64.1 / 64.1 | 699 / 699 / 700 | 2,714 / 2,749 / 2,758 | 4,905 / 4,922 / 4,926
3.0 s | 333 / 334 / 334 | 670 / 670 / 670 | 52.3 / 52.3 / 52.3 | 1,003 / 1,003 / 1,003 | 3,645 / 3,764 / 3,794 | 5,776 / 5,907 / 5,940
5.0 s | 360 / 361 / 361 | 966 / 966 / 966 | 47.6 / 47.6 / 47.7 | 1,326 / 1,326 / 1,326 | 3,670 / 3,777 / 3,804 | 6,123 / 6,145 / 6,150
7.0 s | 366 / 366 / 366 | 1,205 / 1,205 / 1,205 | 45.7 / 45.7 / 45.7 | 1,571 / 1,571 / 1,571 | 4,053 / 4,305 / 4,368 | 6,370 / 6,567 / 6,616
7.5 s | 370 / 370 / 370 | 1,288 / 1,288 / 1,288 | 45.0 / 45.0 / 45.0 | 1,659 / 1,659 / 1,659 | 3,772 / 3,980 / 4,032 | 6,131 / 6,338 / 6,390
Cloud / network / laptop TTS are external; compare SLM TTFT, generation, and TPS across local scheduling conditions—not cloud totals.
Statistics: P50 / P90 / Max · *Gemini cloud completion, not observed last-token time · VAD/last audio excluded · P90 low-confidence (n=2)
11
Notes: This slide shows the non-tool path at a 30% CUDA MPS active-thread cap. The local SLM timings can be compared across local scheduling conditions, but Gemini, Wi-Fi, and laptop OmniVoice timings cannot be controlled by them. Gemini returned a complete non-streamed response, so the cloud milestone is response completion rather than a separately observed last token. P90 is linearly interpolated; the 30% non-tool P90 has only two runs and is descriptive, not a stable tail estimate.

## Slide 12
DEPLOYMENT SUMMARY
Edge SLM is an option—not a requirement
Choose placement from product constraints, not from architecture alone.
Cloud-first is viable
The complete voice pipeline—including the SLM—can run in the cloud. This is the simplest path to deploy and update.
Edge SLM buys locality
Local parsing can support low-latency tool calls, offline operation and tighter control of speech data.
Edge costs engineering
Jetson adds model/runtime compatibility, memory and MPS tuning, monitoring, thermal validation and fleet updates.
Default to cloud; move the SLM to edge only when latency, connectivity, privacy or autonomy justify the extra deployment effort.
Architectural takeaway from the measured Jetson deployment; placement remains a product decision
12
Notes: The whole pipeline can be hosted in the cloud, including the speech-language model. Running the SLM on Jetson is therefore a deliberate product trade-off, not an architectural requirement. Edge placement can improve locality, offline behavior and the bounded tool-call path, but it requires additional compatibility, resource-sharing, thermal and fleet-management work. The benchmark establishes that the edge path is feasible; it does not claim edge placement is always preferable.